## Slide 1: PI_ICR_simulated_data Documentation
Sam Porter (wporter@triumf.ca)
University of British Columbia TRIUMF, on behalf of the TITAN Collaboration

## Slide 2: Overview
Language: MATLAB
PI_ICR_simulated_data.m creates simulated data files based on user-input cyclotron frequencies and accumulation times
Input: Various User Inputs (detailed later)
Output:
  .csv files containing simulated position, time-of-flight and (fake) TDC trigger information
  One .csv file containing an address list of files, their accumulations times (Taccs) and reference files assignments

## Slide 3: User Inputs

## Slide 4: User Inputs
tacc_list: A list of accumulation times you want data simulated for. One file will be made for each Tacc
new_filename: Directory (and filename) to be used
spot_freq_list: A list of cyclotron frequencies of spots you want in the simulated files
  These can be taken from TITAN_spreadsheet.xlsx
R: Average distance from trap center of the spots
pos_deviation: Simulated Gaussian spread of X/Y positions
TOF: Simulated ToF between ejection and detector of counts

## Slide 5: User Inputs
tof_deviation: Simulated Gaussian spread of ToFs
counts_per_spot: Counts to be simulated for each spot (where spots are determined by cyclotron frequency list)
w_minus: Magnetron frequency in trap
amp: Amplitude of the sinusoid dependence (see Automatic Fitting for more explanation)
phase_const: Phase constant of the sinusoid dependence
ref_phase: Phase of the reference (i.e. Tacc = 0) spot

## Slide 6: new_filename
new_filename should be of the form: ~/path/to/directory/filename
  ~/path/to/directory is the directory where files will be saved
  filename will be the name of the FileList.csv
  filenameTacc.csv will be the name of each simulated data file (where Tacc will be the respective Tacc number)
NOTE: When using simulated data with PhIAT.m, make sure Sim Ion Rate is checked and the trap center is set as (0,0)
Once user inputs are done, press the MATLAB run button to create your files!

## Slide 7
For more on PhIAT, please reference the Automatic Fitting documentation
Please contact Sam Porter (wporter@triumf.ca) if you have any questions